## Slide 1: Update on BRSKI-AE – Support for asynchronous enrollment
draft-ietf-anima-brski-async-enroll-04
Steffen Fries, Hendrik Brockhaus, Elliot Lear, David von Oheimb
BRSKI with Pledge in Responder Mode (BRSKI-PRM)
draft-ietf-anima-brski-prm-00
Steffen Fries, Thomas Werner, Elliot Lear, Michael Richardson
Steffen Fries
IETF 112 – ANIMA Working Group

## Slide 2: Discussion on draft split
Original BRSKI-AE discussed two use cases, which have evolved into different directions
Discussion in ANIMA Design Team and on the mailing list to split the draft along the two use cases
UC1 stays as "Support of Asynchronous Enrollment in BRSKI (BRSKI-AE)" covering the application of alternative enrollment protocols. It will cover the description of utilizing other enrollment protocol than EST /simpleenroll in general and using Lightweight CMP specifically. Focus is the interaction between pledge and registrar.
UC2 became "BRSKI with Pledge in Responder Mode (BRSKI- PRM)", and addresses the communication between the pledge and the registrar by reversing the initiator and responder role (compared to RFC 8995) introducing a registrar-agent component to facilitate the communication.
Distinction between operational modes of the pledge
  Pledge-initiator-mode (use case 1): Pledge acts as client and follows the BRSKI approach for the voucher exchange, but allows for alternative enrollment protocols
  Pledge-responder-mode (use case 2): Pledge acts as server and communicates with registrar via a registrar-agent. Pledge is triggered (pushed) to generate and receive bootstrapping data.  main changes made this use case
Draft addresses these issues by defining the call flow and objects to be exchanged. To be independent of the transport security authenticated self-contained objects (signature-wrapped objects) for the certificate enrolment to bind proof of possession and poof of identity to the exchanged objects (similar to existing voucher exchanges with pledge)
11/2/2021
2

## Slide 3: BRSKI-AE Status History of changes
From version 02 to version 03
  Housekeeping, deleted open issue regarding YANG voucher-request in UC2 as voucher-request was enhanced with additional leaf.
  Included open issues of Voucher YANG model in UC2 regarding assertion value agent-proximity and CSR encapsulation using SZTP sub module.
From version 03 to version 04
  Moved UC2 related parts defining the pledge in responder mode to BRSKI-PRM. This required changes and adaptations in several sections including the YANG model (#19).
  Updated references to the Lightweight CMP Profile.
  Change of authors: Added David von Oheimb as co-author. Thomas Werner left.
11/2/2021
3

## Slide 4: BRSKI-AE Next Steps
Clarification of open issues stated in the draft (currently no open issues on ANIMA git)
Further update general description using alternative enrollment protocols and the concrete examples
  Lightweight CMP Profile
  EST with /fullCMC
Updates will be circulated
WG review appreciated
11/2/2021
4

## Slide 5: BRSKI-PRM Status History of changes from BRSKI-AE-03 to BRSKI-PRM-00
Moved UC2 defining the pledge in responder mode from BRSKI-AE-03 to BRSKI-PRM-00. This required changes and adaptations in several sections to remove the description and references to UC1.
Addressed feedback for voucher-request enhancements from YANG doctor early review in Section 6 as well as in the Security Considerations Section.
Renamed ietf-async-voucher-request to ietf-voucher-request-prm in alignment with the new draft and to allow better listing of voucher related extensions; aligned with constraint voucher (#20)
Utilized ietf-voucher-request-prm instead of ietf-voucher-request in voucher exchanges to utilize the enhanced voucher-request (enhanced with additional components).
Included changes from draft-ietf-netconf-sztp-csr-06 regarding the YANG definition of csr-types into the enrollment request exchange.
11/2/2021
5

## Slide 6: BRSKI-PRM Status Next Steps
Further rework the draft (structure and application examples)
Clarification of open issues stated in ANIMA git and also in the draft
Circulate outcome on the mailing list for further discussion
WG review appreciated
11/2/2021
6

## Slide 7: Backup
7

## Slide 8: BRSKI-AE Abstract Protocol Overview
Voucher-request {S/N, reg-cert, …}
S/N verification
Verification of plege signature and IDevID (pledge)
Voucher-request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Issues voucher with assertion proximity
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}
Pledge (caller)
Domain Registrar
Domain CA
MASA
Certification-request
Certification-response (LDevID Cert)
IDevID
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
8
Step1: Voucher request/response handling as in BRSKI
Step2: Application of alternative enrollment protocol, (e.g. Lightweight-CMP
Request CA certificates
CA certificates
Request certificate attributes
Certificate attributes

## Slide 9: BRSKI-PRM Abstract Protocol Overview
Trigger Voucher-request { {reg-cert, agent-signed-data, …}
Voucher-request {S/N, reg-cert, agent-signed-data, …}
Voucher-request {S/N, reg-cert, …}
S/N verification
Verification „reg-cert“ in voucher is own cert
Voucher-request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Issues voucher with assertion agent-proximity
Voucher {reg-cert, assertion, …}
Voucher {reg-cert, assertion, …}
Basement no connectivity to backend
Pledge (callee)
Registrar-Agent
Domain Registrar
Domain CA
MASA
Trigger Enrollment-request
Enrollment-request {signature-wrapped CSR}
Voucher {reg-cert, assertion, …}
Voucher-status
Enrollment-response {LDevID Cert}
Enrollment-status
Enrollment-request (CSR)-request
Enrollment-response (LDevID Cert)
IDevID
LDevID (RegAgt)
LDevID Cert (Reg)
S/N Pledge
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
9
Step1: Collect Bootstrapping request information from pledge
Step2: Infrastructure Interaction based on BRSKI approach to collect voucher and LDevID Cert
Step3: Provisioning of voucher and LDEvID cert to pledge
First floor, connectivity to backend

## Slide 10: Original drawings (just used them as picture as they better scale)
10
Voucher
Request
SN: 1234
Assertion:
proximity
SN: 1234
2021-04-16
Voucher
Request
SN: 1234
Assertion:
proximity
SN: 1234
2021-04-16
Voucher request
Cert
Request
CR
IDevID
BRSKI-PRM
BRSKI-AE
Voucher
Request
SN: 1234
Assertion:
proximity
SN: 1234
2021-04-16
Voucher request
Voucher
Request
SN: 1234
LDevID EE (Reg)
Assertion:
agent-proximity
SN: 1234
2021-04-16
Enroll
Request
IDevID
CSR